## Slide 1: Earth’s Prototype of NASA’s 10-km Earth Blimp: Design, Progress, Schedule and Management Plan
Alex Berka
Valerie Chen
Dietrich Klemm
Umang Lohia
Carlos Valls
Engineering Interns
Team Plane Janes
Space Science Technologies
April 3, 2014

## Slide 2: Introduction
Problem: NASA needs a blimp to survey the Earth’s surface from 10 km
  Carry 100 g camera for a year
  Weigh less than 1 kg
  Fit in 0.23 x 0.56 x 0.91 m container undeployed
  Use only NASA materials
Task
  Design, build, test sea-level Earth prototype of 10-km blimp system
  Design project schedule and management plan
Purpose
  Present design and construction status
  Present team management plan and future timeline

## Slide 3: Summary
Blimp design: Prolate spheroid
  Meets all NASA requirements
  Wide motors and differential thrust for yaw
  Microcontroller controls pitch of motors
  System mass: 706 g/1000 g
Progress
  Blimp complete except fin
  First test flight complete
  To be completed
    Stabilizing membrane fin
    Blimp testing, alterations, and pilot practice
Project on schedule, work evenly divided

## Slide 4
Blimp Design
Side View
Bottom View
Front View
Motor
Gondola
Envelope
Camera Payload
Battery Packs
Membrane Fin
Dowel Rod

## Slide 5
Blimp Design
Front View
Side View
Bottom View
0.98 m
2.55 m
8 in (0.203 m)
12 in (0.305 m)
1.37 m

## Slide 6: Envelope: Provides Lift
Design: Prolate spheroid (football)
  Aspect ratio of 2.5:1 (diameter: length)
  Three internal seams, one external (bottom)
  Gross Lift: 1025 g
  Estimated CD of 0.26
Progress
  Completed full scale envelope
  Need to finish envelope alterations
  Need to attach fin to envelope
0.98m
2.55m

## Slide 7
Gondola constructed out of six Warren trusses
Gondola: Holds Propulsion & Electrical Systems
Bass Wood Chord
Bass Wood Chord
Balsa Wood Struts

## Slide 8
Gondola: Holds Propulsion & Electrical Systems
Stiffness to mass of 1500 N/mg
Guard panels to protect wires
Guard panels
Center Mechanism
1 in (0.03 m)
1 in (0.03 m)
12 in (0.3 m)

## Slide 9: Membrane Fin: Stabilizes Blimp
Intended for yaw stabilization
Made of membrane material
Supported by dowel rod
  Detachable from gondola
Membrane Fin
Front
Back

## Slide 10: Motors: Propel Blimp
6-inch (0.15 m)
propellers
7.25-inch (0.18 m)
circular cardboard
ducts
Bass wood struts
anchor motors
and support ducts
0.5 m dowel rod connects motor
assembly to gondola
Back View
Struts
Dowel
Propeller
7.25 in
(0.18 m)
Motor

## Slide 11: Motors: Control Height
Pitch Control: 180 degrees of freedom
  Allows for movement in solely vertical directions
Side View
Airflow direction
Blimp moves
up
Blimp moves down

## Slide 12: Electrical System: Powers & Controls Blimp
Power - 10 Volts
  2 Battery Packs
  Microcontroller
  Servo
  2 Motors
PWM
  Microcontroller
  2 Motors
  Servo
Battery packs (connected in series)
Top View
Servo
Wires to motors (connected in parallel)
Microcontroller

## Slide 13: Microcontroller: Controls Pitch & Thrust
Microcontroller allows for custom controls
  Left joystick controls differential thrust to both motors
  Right spring-loaded joystick controls pitch
Left
Right
Up
Down
Fast
Slow
Spring-loaded
Joystick
Regular
Joystick

## Slide 14: System Integration
Detachable motor assemblies
Center mechanism attaches to servo
Central dowel rod runs through membrane loops on envelope
Membrane shroud surrounds gondola
Side View
Bottom View
Motor Detachment Points
Membrane Shroud:
Fastens gondola to envelope

## Slide 15: Mass Budget Under 1 kg
System | Component | Mass (g)
Payload | Camera | 100
Envelope | Envelope and Shroud Lines | 113.76
Gondola | Gondola Frame | 53.49
 | Stabilization Fin | 30
Propulsion | Right Motor Assembly | 59.46
 | Left Motor Assembly | 55.11
 | Pulley Assembly | 42.73
Electronics | Battery Pack A | 73.53
 | Battery Pack B | 71.27
 | Microcontroller | 33.38
 | Wires | 13.50
 | Receiver | 9.63
Ballast | Ballast | 50
Total |  | 706

## Slide 16: Predicted Lift and Speed
Gross lift of 1025 g
Currently over-lifts
Maximum speed estimated at 3.45 m/s
Speed Calculations

## Slide 17
Chart: 
| Team Oral Presentation on Blimp Design | Blimp Fabrication/Testing | Gondola Fabrication | Motors/Propellers/Ducts | Electronics (Microcontroller Programming) | Electronics (Wiring) | Envelope Fabrication/Shroud Lines | Blimp Testing
START DATE | 41708 | 41712 | 41714 | 41714 | 41720 | 41720 | 41723 | 41724
DURATION | 4 | 13 | 2 | 2 | 2 | 2 | 1 | 1
Oral Pres.: Blimp Design
Blimp Fabrication
Gondola Fabrication
Motor/Propellers/Ducts
Microcontroller
Electronics and Wiring
Envelope/Shroud Lines
Blimp Testing
Completed
Blimp Project Schedule, March 2014

## Slide 18
Chart: 
| Team Blimp Written Progress Report | Demonstration Flight | Team Oral Presentation on Blimp Progress | Blimp Testing and Alterations | Qualification Flight | Final Team Presentation | Blimp Competition | Final Team Report
START DATE | 41716 | 41725 | 41725 | 41730 | 41732 | 41733 | 41741 | 41742
DURATION | 6 | 1 | 6 | 3 | 1 | 8 | 1 | 8
Written Progress Report
Demonstration Flight
Oral Pres.: Blimp Progress
Blimp Testing/Alterations
Qualification Flight
Final Oral Presentation
Blimp Competition
Final Team Report
Blimp Project Schedule, March-April 2014

## Slide 19: Management and Task Responsibilities
Name | Reporting Management | Construction Management | Hands-on Construction
Alex Berka | Final Report | Motor Ducts | Motor Ducts, Gondola
Valerie Chen | Blimp Written Progress Report | Gondola | Gondola, Envelope
Dietrich Klemm | Final Presentation | Electronics: Microcontroller Programming | Wiring, Microcontroller
Umang Lohia | Presentation on Blimp Progress | Electronics & Wiring | Wiring, Envelope
Carlos Valls | Presentation on Blimp Design | Envelope | Envelope, Gondola
*Note that all members contributed to all reporting assignments

## Slide 20: Conclusion
Blimp design: Prolate spheroid
  Meets all NASA requirements
  Wide motors and differential thrust for yaw
  Microcontroller controls pitch of motors
  System mass: 672.95 g/1000 g
Progress
  Blimp complete except fin
  First test flight complete
  To be completed
    Stabilizing membrane fin
    Blimp testing, alterations, and pilot practice
Project on schedule, work evenly divided

## Slide 21: Estimating Thrust
Figure produced by Alex Berka from lab data
Chart: 6 in Propellers Produce Max Thrust of 0.68N
| 0.88800000000000001 | 0.99199999999999999 | 1.0960000000000001 | 1.1839999999999999 | 1.248 | 1.3120000000000001 | 1.3839999999999999 | 1.456 | 1.504 | 1.544 | 1.7
5 inch | 0.00016707 | 0.030064 | 0.081064 | 0.13119 | 0.17339 | 0.2156 | 0.25956 | 0.30705 | 0.36332 | 0.40993 | 0.48379
6 inch | 0.00084769 | 0.023871 | 0.072011 | 0.14318 | 0.23946 | 0.3169 | 0.43516 | 0.5869 | 0.66853
7 inch | 0.00229 | 0.10908 | 0.25148 | 0.47853 | 0.72868
7 in Propeller
6 in Propeller
5 in Propeller

## Slide 22: Estimating CD
Chart created by Prof. Washabaugh: Lab 06 Thrust vs Drag